## Slide 1
Prioritization Framework: Selecting Our Pilot State
Ranked on cost, ease of implementation, timeframe, and impact — not relationship strength alone
State | Ease of Entry | Timeframe | Impact | Role
California | High — mature market, proven model | Immediate | Validates the concept works | Proof It Works
North Carolina | Medium — Duke already moving this direction | 1-2 years | Demonstrates real customer demand (PowerPair waitlisted) | Proof Demand Exists
Michigan | High — vertically integrated utility, statutory mandate | Year 1 pilot | Worst outages in the nation + 2,500 MW storage mandate (2029 deadline) | RECOMMENDED PILOT
Why Michigan Wins on the Numbers
Reliability: 50th of 51 states in outage duration (~18 hrs/customer/yr) — and outages are distribution-level, exactly what a home battery covers.
Policy hook: 2023 state law (PA 235) mandates 2,500 MW of storage with utility compliance filings due by 2029 — a ready-made rate-basing vehicle.
Ownership structure: DTE and Consumers are vertically integrated and can legally rate-base batteries directly (unlike deregulated Illinois).
Competition: Near-greenfield — one small pilot exists; no scaled residential program.
Note: Wisconsin (strongest APTIM relationship) and Illinois (best raw capacity pricing) were evaluated and held as expansion markets — see appendix.
Confidential. Not to be copied, distributed, or reproduced without prior approval. © 2026 APTIM - All rights reserved.
1

## Slide 2
Service Concept: Utility-Owned Battery + Solar Fleet
The utility owns the fleet. APTIM administers it. The customer pays nothing.
Hardware Maker
Tesla / Enphase / equivalent
Makes the physical battery + solar hardware
Asset Owner + Dispatcher
The Utility
Finances, owns, and rate-bases the fleet as grid infrastructure; dispatches via Tesla/EnergyHub software; captures avoided peak-capacity value ($500-$1,500/kW)
Program Administrator (APTIM)
APTIM
Site selection, household recruitment, hosting agreements, contractor network management, installation QA, fleet reporting, regulatory compliance
→
→
Revenue Model
Utility earns: Regulated rate-of-return on rate-based capital, plus avoided peaker/T&D deferral value
APTIM earns: Level-of-effort administration fee — insulated from hardware price swings
Household earns: Free backup power + lower bills; zero cost, zero maintenance
O&M funded by: Dispatch value ($500-$1,500/kW avoided capacity cost) — the asset funds its own upkeep
Why the Client Says Yes
Utility: Cheaper peak capacity than a new peaker plant; grows rate base; meets Michigan's statutory storage mandate
Household: Backup power during a storm-prone state's worst-in-nation outages — at zero cost
Regulator: Resilience delivered to vulnerable communities without a new tax or appropriation
Confidential. Not to be copied, distributed, or reproduced without prior approval. © 2026 APTIM - All rights reserved.
2